## Slide 1: Leveraging Azure Digital Twins in a supply chain

## Slide 2: Abstract and learning objectives
In this whiteboard design session, you will work in a group to evaluate Contoso's goals and design an IoT-based supply chain solution that uses the optimal combination of Azure tools and services that will fulfill their needs. You will also model their physical and logical environment to identify elements along with their properties and define the relationships between them. You will guide Contoso on deploying these models to Azure Digital Twins, how to leverage them and keep them up-to-date.
At the end of this whiteboard design session, you will be better able to design an end-to-end Azure IoT supply chain solution from telemetry ingestion to data insights, all while leveraging Azure Digital Twins.

## Slide 3: Step 1: Review the customer case study
Outcome
Analyze your customer needs
Timeframe
15 minutes

## Slide 4: Customer situation
Contoso Apparel is a multinational clothing manufacturer
Product quality is directly correlated to humidity
Desire to model, visualize, and query the state of their supply chain
Implement custom factory failover logic
Notes: Contoso Apparel is a large multinational clothing manufacturer. Their environment consists of several factories, warehouses, storefronts, and logistics infrastructure. Multiple telemetry points are measured to ensure the highest quality level in their products, such as temperature, vibration, location, and humidity. Of these readings, maintaining humidity within the range of X and Y at all supply chain levels is the most critical. Due to mold issues, humidity has a direct correlation to the quality of the delivered consumer end-product.
Contoso Apparel is looking to implement an end-to-end IoT solution in Azure. They will need data ingestion, processing, storage, and visualization. For the proof of concept, they wish to track humidity levels at each level of their supply chain to ensure a high-quality consumer product.
Contoso desires to model and visualize the relationship between their processes, products, equipment, factories, shipping logistics, warehouses, and storefronts. They wish to have the ability to query into the current state of each of these elements defined their supply chain environment. They would also like to analyze historical data to track successful product deliveries or determine the root cause of unsuccessful deliveries. They also wish to leverage these models to simulate potential 'what if' process changes and assess their overall impact without experimenting with or impacting the current supply chain.
In this proof of concept project, Contoso Apparel also wants to improve resiliency and time to recover at their factories by automating mitigating measures should an anomalous event occur. For example, product manufacturing could be re-routed to a secondary 'failover' factory should there be a moisture problem at the original facility. Currently, this type of failover is a manual, lengthy, and error-prone process that involves updating several systems and configuration files.

## Slide 5: Customer needs
We would like to model our supply chain environment in order to gain insight into the elements along with their properties, components and the relationships between them.
We need monitor humidity telemetry from our factories in near real-time for anomalies between the values of X and Y. What services can we put in place so that we can quickly be alerted when this happens?
We would like the ability to re-route manufacturing to a different facility should there be a moisture problem at a factory.
We need the ability to query the current state of our supply chain elements.
We need the ability to review historical trends in data to identify what is working well as well as for root cause analysis of problems. We need to be able to perform ad-hoc queries on this data and obtain customized chart visualizations.

## Slide 6: Customer objections
Authoring Digital Twin Definition Language (DTDL) documents for all of our supply chain elements sounds like an enormous and complex undertaking. We don't even know how to get started with this. What do you recommend as a starting point?
Our supply chain is a continuously running system, 24 hours a day, 7 days a week. As such, the state of each of our elements is in a constant state of change. How can we ensure the accuracy of our digital models? How will these be kept up-to-date?
We want to track a manufactured product such as a T-Shirt from its manufacturing on a factory floor, delivery to a warehouse, then to a store. Finally, we'd like to trace the T-Shirt through its purchase at a store by a customer. Is this level of tracing even possible?

## Slide 7: Common scenarios
Notes: Azure Digital Twins is commonly used in combination with other Azure services as part of a larger IoT solution. A complete solution using Azure Digital Twins may contain the following parts:
The Azure Digital Twins service instance. This stores your twin models and your twin graph with its state, and orchestrates event processing.
One or more client apps that drive the Azure Digital Twins instance by configuring models, creating topology, and extracting insights from the twin graph.
One or more external compute resources to process events generated by Azure Digital Twins, or connected data sources such as devices. One common way to provide compute resources is via Azure Functions.
An IoT hub to provide device management and IoT data stream capabilities. Downstream services to handle tasks such as workflow integration (like Logic Apps, cold storage, time series integration, or analytics).

## Slide 8: Step 2: Design the solution
Outcome
Design a solution and prepare to present the solution to the target customer audience in a 15-minute chalk-talk format.
Timeframe
60 minutes
Business needs (10 minutes) | Respond to questions outlined in your guide and list the answers on a flipchart
Design (35 minutes) | Design a solution for as many of the stated requirements as time allows. Show the solution on a flipchart
Prepare (15 minutes) | Identify any customer needs that are not addressed with the proposed solution Identify the benefits of your solution Determine how you will respond to the customer’s objections Prepare for a 15-minute presentation to the customer

## Slide 9: Step 3: Present the solution
Outcome
Present a solution to the target customer in a 15-minute chalk-talk format
Timeframe
30 minutes (15 minutes for each team to present and receive feedback)
Directions
Pair with another table
One table is the Microsoft team and the other table is the customer
The Microsoft team presents their proposed solution to the customer
The customer asks one of the objections from the list of objections in the case study
The Microsoft team responds to the objection
The customer team gives feedback to the Microsoft team

## Slide 10: Wrap-up
Outcome
Identify the preferred solution for the case study
Identify solutions designed by other teams
Timeframe
15 minutes

## Slide 11: Preferred target audience
Courtney Laval, Chief Technical Officer (CTO), Contoso Apparel.
The primary audience is the business decision makers and technology decision makers. From the case study scenario, this includes Courtney Laval, CTO of Contoso Apparel. Usually we talk to the infrastructure managers who report to the chief information officers (CIOs), or to application sponsors (like a vice president [VP] line of business [LOB], or chief marketing officer [CMO]), or to those who represent the business unit IT or developers that report to application sponsors.

## Slide 12: Preferred solution – High-level architecture
Notes: IoT sensors in Contoso Apparel's environment send telemetry into IoT Hub via a device connection string. An Azure Function is triggered on message ingestion to process the incoming telemetry and updates the appropriate digital twin in the Azure Digital Twins service. A route is established between the Azure Digital Twins Service and a second Azure Function so that the telemetry stream is made available to the SignalR service. Web applications are then able to subscribe to this SignalR hub to receive telemetry information. A secondary route is established between the Azure Digital Twins service and an Event Hub intermediary to provide data into Time Series Insights via a third Azure Function.

## Slide 13: Preferred solution – Environment Modeling (1)
1) As a starting point, how do you recommend Contoso Apparel approach modeling entities in their environment?
Ontologies provide a great starting point for digital twin solutions. They encompass a set of domain-specific models and relationships between entities for designing, creating, and parsing a digital twin graph.
Notes: 1) As a starting point, how do you recommend Contoso Apparel approach modeling entities in their environment?
Ontologies provide a great starting point for digital twin solutions. They encompass a set of domain-specific models and relationships between entities for designing, creating, and parsing a digital twin graph. The ontologies provided by Microsoft are also designed to be easily extensible, so that you can customize them for your solution. There are three possible strategies for integrating industry-standard ontologies with DTDL. Adopt, you can start your solution with an open-source DTDL ontology that has been built on widely adopted industry standards. You can either use these model sets out-of-the-box, or extend them with your own additions for a customized solution. Convert, if you already have existing models represented in another standard format, you can convert them to DTDL to use them with Azure Digital Twins. Author, you can always develop your own custom DTDL models from scratch, using any applicable industry standards as inspiration.

## Slide 14: Preferred solution – Environment Modeling (2)
2) At a high level, what types of information should be encapsulated within an entity definition?
Within a model definition, the top-level code item is an interface. This encapsulates the entire model, and the rest of the model is defined within the interface. A DTDL model interface may contain zero, one, or many of each of the following fields:
Property
Telemetry
Component
Relationship
Notes: 2) At a high level, what types of information should be encapsulated within an entity definition?
Within a model definition, the top-level code item is an interface. This encapsulates the entire model, and the rest of the model is defined within the interface. A DTDL model interface may contain zero, one, or many of each of the following fields:
Property: Properties are data fields that represent the state of an entity (like the properties in many object-oriented programming languages). Properties have backing storage and can be read at any time. Properties are expected to have backing storage. This means that you can read a property at any time and retrieve its value. If the property is writeable, you can also store a value in the property.
Telemetry: Telemetry fields represent measurements or events, and are often used to describe device sensor readings. Unlike properties, telemetry is not stored on a digital twin; it is a series of time-bound data events that need to be handled as they occur. For more on the differences between property and telemetry, see the Properties vs. telemetry section below. Telemetry is more like a stream of events; it's a set of data messages that have short lifespans. If you don't set up listening for the event and actions to take when it happens, there is no trace of the event at a later time. You can't come back to it and read it later.
Component: Components allow you to build your model interface as an assembly of other interfaces, if you want. An example of a component is a frontCamera interface (and another component interface backCamera) that are used in defining a model for a phone. You must first define an interface for frontCamera as though it were its own model, and then you can reference it when defining Phone. Use a component to describe something that is an integral part of your solution but doesn't need a separate identity, and doesn't need to be created, deleted, or rearranged in the twin graph independently. If you want entities to have independent existences in the twin graph, represent them as separate digital twins of different models, connected by relationships (see next bullet).
Relationship - Relationships let you represent how a digital twin can be involved with other digital twins. Relationships can represent different semantic meanings, such as contains ("floor contains room"), cools ("hvac cools room"), isBilledTo ("compressor is billed to user"), etc. Relationships allow the solution to provide a graph of interrelated entities.

## Slide 15: Preferred solution – Environment Modeling (3)
3) What methods are available for Contoso to add these entities to their environment knowledge graph?
- Data plane APIs are the Azure Digital Twins APIs used to manage the elements within your Azure Digital Twins instance.
- SDKs supporting languages such as C#, Java, JavaScript, and Python.
- Digital Twins Explorer application
Notes: 3) What methods are available for Contoso to add these entities to their environment knowledge graph?
Data plane APIs are the Azure Digital Twins APIs used to manage the elements within your Azure Digital Twins instance. They include operations like creating routes, uploading models, creating relationships, and managing twins.These are available as REST APIs. Calling these APIs is also made available via a variety of SDKs supporting languages such as C#, Java, JavaScript, and Python. Calling these APIs are automated in the Digital Twins Explorer application if you desire a user interface to upload your models.
The data plane APIs can be broadly divided into the following categories:
DigitalTwinModels - The DigitalTwinModels category contains APIs to manage the models in an Azure Digital Twins instance. Management activities include upload, validation, retrieval, and deletion of models authored in DTDL.
DigitalTwins - The DigitalTwins category contains the APIs that let developers create, modify, and delete digital twins and their relationships in an Azure Digital Twins instance.
Query - The Query category lets developers find sets of digital twins in the twin graph across relationships.
Event Routes - The Event Routes category contains APIs to route data, through the system and to downstream services.

## Slide 16: Preferred solution – Environment Modeling (4)
4) How would Contoso query and visualize the knowledge graph representation of their environment model?
Contoso would use Azure Digital Twins query language to query their twin graph, using the Query API, SDK, or inside of the Azure Digital Twins Explorer application. For visualizing the twin graph, they would use the Azure Digital Twins Explorer.
Notes: 4) How would Contoso query and visualize the knowledge graph representation of their environment model?
Contoso would use Azure Digital Twins query language to query their twin graph, using the Query API, SDK, or inside of the Azure Digital Twins Explorer application. For visualizing the twin graph, they would use the Azure Digital Twins Explorer.

## Slide 17: Preferred solution – Data ingestion and modeling (1)
1) Which Azure service(s) should Contoso use to register and authenticate their IoT devices?
Contoso Apparel should use IoT Hub, or the combination of IoT Hub and the Device Provisioning Service (DPS) to register and authenticate their IoT devices.
Notes: 1) Which Azure service(s) should Contoso use to register and authenticate their IoT devices?
Contoso Apparel should use IoT Hub, or the combination of IoT Hub and the Device Provisioning Service (DPS) to register and authenticate their IoT devices

## Slide 18: Preferred solution – Data ingestion and modeling (2)
2) How should the IoT telemetry data be ingested into Azure?
Data should be ingested via IoT Hub alongside an Azure Function compute resource that processes the telemetry and updates the digital twin model.
Notes: Data should be ingested via IoT Hub alongside an Azure Function compute resource that processes the telemetry and updates the digital twin model.

## Slide 19: Preferred solution – Data ingestion and modeling (3)
3) How would Contoso Apparel monitor for humidity anomalies in near real-time?
Event routing
Notes: Contoso can subscribe to the Digital Twin Telemetry Messages notification type and route those to Event Grid for further processing. Event routes are also used to handle events within the twin graph and send data from digital twin to digital twin. This is done by connecting event routes through Event Grid to compute resources, such as Azure Functions. These functions then define how twins should receive and respond to events. Alternatively, Contoso Apparel could use Azure Stream Analytics to monitor for anomalies in near real-time, either using a query to find telemetry out of range, or utilizing the built-in anomaly detection capabilities.

## Slide 20: Preferred solution – Data ingestion and modeling (4)
4) Which Azure service(s) would you recommend so that Contoso Apparel can receive the humidity anomaly notification?
A Logic Application could be used to provide a number of notification types, including email and text message notifications.
Notes: 4) Which Azure service(s) would you recommend so that Contoso Apparel can receive the humidity anomaly notification?
A Logic Application could be used to provide a number of notification types, including email and text message notifications.

## Slide 21: Preferred solution – Model updates (1)
1) How do you suggest keeping the environment model up-to-date with the real world state?
An Azure Function can process incoming telemetry and forward this information to Azure Digital Twins
Notes: Preferred solution – Model updates (1)
To keep the live execution environment of Azure Digital Twins up to date with the real world, you can use IoT Hub and an Azure Function to connect your solution to IoT and IoT Edge devices. These hub-managed devices are represented as part of your twin graph and provide the data that drives your model. You can also update Azure Digital Twins from other data sources that are able to use REST APIs (and SDKs) or with connectors to other services like Logic Apps.

## Slide 22: Preferred solution – Business logic implementation(1)
1) How do you suggest implementing failover in the event that a factory needs to be taken offline for maintenance?
An Azure Function can subscribe to Azure Digital Twin update events and execute custom failover logic when appropriate.
Notes: 1) How do you suggest implementing failover in the event that a factory needs to be taken offline for maintenance?
The Azure Digital Twins service supports the creation of event routes to send event data to custom-defined endpoints in your subscriptions. One supported event type is the Digital Twin Change Notification (Microsoft.DigitalTwins.Twin.Update) that is emitted every time a digital twin property changes. An event route can be configured to feed updates through an event hub that triggers an Azure Function for further processing. This Azure Function can monitor for a factory becoming offline and contain the custom business logic required to perform the failover.

## Slide 23: Preferred solution – Data Visualization (1)
1) Contoso apparel needs to be able to perform ad-hoc queries and visualize historical data. What Azure service(s) would you suggest for this?
Azure Time Series Insights allows for ad-hoc queries and visualization of historical data.
Notes: Azure Time Series insights allows for ad-hoc queries and visualization of historical data. Alternatively, data could be forwarded to other analysis services such as Azure Synapse Analytics to take advantage of visualization capabilities such as serverless SQL, Apache Spark, and Power BI.

## Slide 24: Preferred objections handling (1)
1) Authoring Digital Twin Definition Language (DTDL) documents for all of our supply chain elements sounds like an enormous and complex undertaking. We don't even know how to get started with this. What do you recommend as a starting point?
Constoso Apparel could adopt existing Digital Twin ontologies as a starting point to defining the elements in their environment. These ontologies are also extensible so that they have the ability to define their own custom features in their models.
Notes: 1) Authoring Digital Twin Definition Language (DTDL) documents for all of our supply chain elements sounds like an enormous and complex undertaking. We don't even know how to get started with this. What do you recommend as a starting point?
Constoso Apparel could adopt existing Digital Twin ontologies as a starting point to defining the elements in their environment. These ontologies are also extensible so that they have the ability to define their own custom features in their models.

## Slide 25: Preferred objections handling (2)
2) Our supply chain is a continuously running system, 24 hours a day, 7 days a week. As such, the state of each of our elements is in a constant state of change. How can we ensure the accuracy of our digital models? How will these be kept up-to-date?
Contoso should leverage an Azure Function integration between IoT Hub and Azure Digital Twins as a way to keep their digital models up to date. They can also update Azure Digital Twins from other data sources that are able to use REST APIs (and SDKs) or with connectors to other services like Logic Apps.
Notes: 2) Our supply chain is a continuously running system, 24 hours a day, 7 days a week. As such, the state of each of our elements is in a constant state of change. How can we ensure the accuracy of our digital models? How will these be kept up-to-date?
Constoso Apparel could adopt existing Digital Twin ontologies as a starting point to defining the elements in their environment. These ontologies are also extensible so that they have the ability to define their own custom features in their models.

## Slide 26: Preferred objections handling (3)
3) We want to track a manufactured product such as a T-Shirt from its manufacturing on a factory floor, delivery to a warehouse, then to a store. Finally, we'd like to trace the T-Shirt through its purchase at a store by a customer. Is this level of tracing even possible?
A Digital Twin instance can be created for the T-Shirt, through event routing data can be sent to Azure Time Series Insights for historical analysis. Alternatively, custom apps can also receive these updates and provide customized visualizations.
Notes: 3) We want to track a manufactured product such as a T-Shirt from its manufacturing on a factory floor, delivery to a warehouse, then to a store. Finally, we'd like to trace the T-Shirt through its purchase at a store by a customer. Is this level of tracing even possible?
Yes! Create a digital twin instance for the T- Shirt. Using Azure Digital Twins Explorer, you can initiate a query to obtain the current status of the twin. Create an event route so that twin updates are sent to Azure Time Series Insights (via an Event Hub and an Azure Function). Azure Time Series insights allow for retrieving historical data based on the digital twin instance to view its state over time, including the ability to view this information in tabular format. As an alternative, an Azure Function can implement logic to store T-Shirt lifecycle information in a data store that serves a custom web application. This web application can implement custom visualizations and receive twin updates near real-time via SignalR.

## Slide 27: Customer quote
"When we started looking into modeling our existing IoT environment, it felt like we were to embark on an extremely complicated, proprietary, and lengthy process. We are pleasantly surprised with how we were quickly able to grasp DTDL and the many different approaches we can take to ensure our digital twins are up to date. We now have an architecture in place that allows us to not only query the current state of our environment, but we also have the ability to push updates to other visualization tools like Azure Time Series Insights, and our web applications by leveraging SignalR!"
Courtney Laval, Chief Technical Officer (CTO), Contoso Apparel.

## Slide 28: End